## Slide 1: Computer Networks
By Sadiq Shah
Lecture 5
(Chapter 2)
FATA University

## Slide 2: Description of Layers (TCP/IP Protocol Suite)

## Slide 3: 1. Physical Layer
Physical layer is responsible for carrying individual bits in a frame across the link.
There is another, hidden layer, the transmission media, under the physical layer.
Two devices are connected by a transmission medium (cable or air).
We need to know that the transmission medium does not carry bits; it carries electrical or optical signals.
So the bits received in a frame from the data-link layer are transformed and sent through the transmission media, but we can think that the logical unit between two physical layers in two devices is a bit

## Slide 5: 2. Data-link Layer
The routers are responsible for choosing the best links.
the data-link layer is responsible for taking the datagram and moving it across the link.
The link can be a wired LAN with a link-layer switch, a wireless LAN, a wired WAN, or a wireless WAN.
The data-link layer takes a datagram and encapsulates it in a packet called a frame.

## Slide 6: 3. Network Layer
The network layer is responsible for creating a connection between the source computer and the destination computer. The communication at the network layer is host-to-host.
However, since there can be several routers from the source to the destination, the routers in the path are responsible for choosing the best route for each packet
The network layer in the Internet includes the main protocol, Internet Protocol (IP), that defines the format of the packet, called a datagram at the network layer.
IP also defines the format and the structure of addresses used in this layer.

## Slide 7
The network layer also has some auxiliary protocols that help IP in its delivery and routing tasks.
The Internet Control Message Protocol (ICMP) helps IP to report some problems when routing a packet.
The Internet Group Management Protocol (IGMP) is another protocol that helps IP in multitasking.
The Dynamic Host Configuration Protocol (DHCP) helps IP to get the network-layer address for a host.
The Address Resolution Protocol (ARP)

## Slide 8: 4. Transport Layer
The logical connection at the transport layer is also end-to-end.
The transport layer at the source host gets the message from the application layer, encapsulates it in a transport layer packet (called a segment or a user datagram in different protocols) and sends it,
In other words, the transport layer is responsible for giving services to the application layer: to get a message from an application program running on the source host transport-layer protocols in the Internet, each designed for some specific task.
The main protocol, Transmission Control Protocol (TCP), and UDP (User Datagram Protocol (UDP))

## Slide 9: 5. Application Layer
The two application layers exchange messages between each other as though there were a bridge between the two layers.
However, we should know that the communication is done through all the layers.
Communication at the application layer is between two processes (two programs running at this layer).
To communicate, a process sends a request to the other process and receives a response.

## Slide 10: Protocols of App layer
The Hypertext Transfer Protocol (HTTP) is a vehicle for accessing the World Wide Web (WWW).
The Simple Mail Transfer Protocol (SMTP) is the main protocol used in electronic mail (e-mail) service.
The File Transfer Protocol (FTP) is used for transferring files from one host to another.
The Terminal Network (TELNET) and Secure Shell (SSH) are used for accessing a site remotely.
The Simple Network Management Protocol (SNMP) is used by an administrator to manage the Internet at global and local levels.

## Slide 11: Encapsulation and Decapsulation

## Slide 12: Encapsulation at the Source Host
At the source, we have only encapsulation.
At the application layer, the data to be exchanged is referred to as a message. A message normally does not contain any header or trailer. The message is passed to the transport layer.
The transport layer takes the message as the payload, the load that the transport layer should take care of. It adds the transport layer header to the payload which contains the identifiers of the source and destination application programs

## Slide 13: Encapsulation at the Source…..
The result is the transport-layer packet, which is called the segment (in TCP) and the user datagram (in UDP). The transport layer then passes the packet to the network layer.
3. The network layer takes the transport-layer packet as data or payload and adds its own header to the payload.
The header contains the addresses of the source and destination hosts
The result is the network-layer packet, called a datagram.
The network layer then passes the packet to the data-link layer.

## Slide 14: Encapsulation at the Source…..
4. The data-link layer takes the network-layer packet as data or payload and adds its own header, which contains the link-layer addresses of the host or the next hop (the router). The result is the link-layer packet, which is called a frame.
The frame is passed to the physical layer for transmission.

## Slide 15: Decapsulation and Encapsulation at the Router

## Slide 16: Decapsulation and Encapsulation at the Router
At the router, we have both decapsulation and encapsulation because the router is connected to two or more links.
1. After the set of bits are delivered to the data-link layer, this layer decapsulates the datagram from the frame and passes it to the network layer.
2. The network layer only inspects the source and destination addresses in the datagram header and consults its forwarding table to find the next hop to which the datagram is to be delivered.
The datagram is then passed to the data-link layer of the next link.
3. The data-link layer of the next link encapsulates the datagram in a frame and passes it to the physical layer for transmission.

## Slide 17: Decapsulation at the Destination Host
At the destination host, each layer only decapsulates the packet received, removes the payload, and delivers the payload to the next-higher layer protocol until the message reaches the application layer