## Slide 1: Computer Networks
By Sadiq Shah
Lecture 6
(Chapter 2)
FATA University

## Slide 2: Addressing

## Slide 3
At the application layer, we normally use names to define the site that provides services, such as someorg.com, or the e-mail address, such as sadiqshah@fu.edu.pk
At the transport layer, addresses are called port numbers, and these define the application-layer programs at the source and destination.
Port numbers are local addresses that distinguish between several programs running at the same time. E.g 80, 25
At the network-layer, the addresses are global, with the whole Internet as the scope. That is IP Address like 50.98.50.1 (IPv4=32bits, IPv6=128bits)

## Slide 4
The link-layer addresses, sometimes called MAC addresses, are locally defined addresses:
MAC addresses are 12-digit hexadecimal numbers (48 bits in length)
E.g 00:1B:44:11:3A:B7
1 hex digit= 4bits
12 hex = 48bits

## Slide 5: THE OSI MODEL
International Organization for Standardization (ISO) is a multinational body dedicated to worldwide agreement on international standards
An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model.

## Slide 6
The OSI model is not a protocol; it is a model for understanding and designing a network architecture
It consists of seven separate but related layers, each of which defines a part of the process of moving information across a network

## Slide 8: OSI versus TCP/IP
When we compare the two models, we find that two layers, session and presentation, are missing from the TCP/IP protocol suite

## Slide 9: Quiz no. 1
Q1: Which layers of the TCP/IP protocol suite are involved in a link-layer switch?
Q2: A host communicates with another host using the TCP/IP protocol suite. What is the unit of data sent or received at each of the following layers?
a. application layer b. network layer c. data-link layer
Q3: What are the types of addresses (identifiers) used in each of the following layers?
a. application layer b. network layer c. data-link layer