## Slide 1: Computer Networks
By Sadiq Shah
Lecture 7
(Chapter 3)
FATA University

## Slide 2
Physical Layer

## Slide 3: Introduction to Physical Layer
DATA AND SIGNALS

## Slide 4
Alice and Bob need to exchange data, communication at the physical layer means exchanging signals.
Data need to be transmitted and received, but the media have to change data to signals.
Both data and the signals that represent them can be either analog or digital in form.
Switches are also involved in the physical communication.

## Slide 5: Analog and Digital Data
Data can be analog or digital.
The term analog data refers to information that is continuous; digital data refers to information that has discrete states.
  For example, an analog clock that has hour, minute, and second hands gives information in a continuous form; the movements of the hands are continuous.
On the other hand, a digital clock that reports the hours and the minutes will change suddenly from 8:05 to 8:06.
Analog data, such as the sounds made by a human voice, take on continuous values.
Digital data take on discrete values. For example, data are stored in computer memory in the form of 0s and 1s.

## Slide 6: Analog and Digital Signals
Like the data they represent, signals can be either analog or digital.
An analog signal has infinitely many levels of intensity over a period of time.
As the wave moves from value A to value B, it passes through and includes an infinite number of values along its path.
A digital signal, on the other hand, can have only a limited number of defined values.
The simplest way to show signals is by plotting them on a pair of perpendicular axes.
  The vertical axis represents the value or strength of a signal.
  The horizontal axis represents time.

## Slide 8: Periodic and Nonperiodic
Both analog and digital signals can take one of two forms: periodic or nonperiodic (aperiodic).
  A periodic signal completes a pattern within a measurable time frame, called a period, and repeats that pattern over subsequent identical periods.
The completion of one full pattern is called a cycle.
  A nonperiodic signal changes without exhibiting a pattern or cycle that repeats over time.
Both analog and digital signals can be periodic or nonperiodic.

## Slide 10: PERIODIC ANALOG SIGNALS
Periodic analog signals can be classified as simple or composite.
A simple periodic analog signal, a sine wave, cannot be decomposed into simpler signals.
A composite periodic analog signal is composed of multiple sine waves.
Sine Wave
The sine wave is the most fundamental form of a periodic analog signal.
When we visualize it as a simple oscillating curve, its change over the course of a cycle is smooth and consistent, a continuous, rolling flow.

## Slide 11
A sine wave can be represented by three parameters: the peak amplitude, the frequency, and the phase.

## Slide 12
Peak Amplitude
The peak amplitude of a signal is the absolute value of its highest intensity, proportional to the energy it carries. For electric signals, peak amplitude is normally measured in volts.

## Slide 13
Period and Frequency
Period refers to the amount of time, in seconds, a signal needs to complete 1 cycle.
Frequency refers to the number of periods in 1 s.
Note that period and frequency are just one characteristic defined in two ways.
Period is the inverse of frequency, and frequency is the inverse of period, as the following formulas show.
Period is formally expressed in seconds. Frequency is formally expressed in Hertz (Hz), which is cycle per second.

## Slide 14
End of Lecture