## Slide 1: Computer Networks
By Sadiq Shah
Lecture 11
(Chapter 18)
FATA University

## Slide 2
Network Layer-Part 1

## Slide 3: NETWORK-LAYER SERVICES
The network layer in the TCP/IP protocol suite is responsible for the host-to-host delivery of datagrams.
It provides services to the transport layer and receives services from the data-link layer.
network-layer services
1. Packetizing
The first duty of the network layer is definitely packetizing.
duty of the network layer is to carry a payload from the source to the destination without changing it or using it.
The network layer is doing the service of a carrier such as the postal office, which is responsible for delivery of packages from a sender to a receiver without changing or using the contents.

## Slide 4
2. Routing and Forwarding
  Routing
The network layer is responsible for routing the packet from its source to the destination.
A physical network is a combination of networks (LANs and WANs) and routers that connect them. This means that there is more than one route from the source to the destination.
The network layer is responsible for finding the best one among these possible routes.
In the Internet today, this is done by running some routing protocols e.g RIP OSPF etc.

## Slide 5
Forwarding
Forwarding can be defined as the action applied by each router when a packet arrives at one of its interfaces.
The decision-making table a router normally uses for applying this action is sometimes called the forwarding table and sometimes the routing table.
When a router receives a packet from one of its attached networks, it needs to forward the packet to another attached network

## Slide 7: NETWORK-LAYER PERFORMANCE
The performance of a network can be measured in terms of delay, throughput, and packet loss.
1. Delay
The delays in a network can be divided into four types: transmission delay, propagation delay, processing delay, and queuing delay.
Transmission delay
A sender needs to put the bits in a packet on the line one by one.
If the first bit of the packet is put on the line at time t1 and the last bit is put on the line at time t2, transmission delay of the packet is (t2 − t1).
Definitely, the transmission delay is longer for a longer packet and shorter if the sender can transmit faster.

## Slide 8
Propagation Delay
Propagation delay is the time it takes for a bit to travel from point A to point B in the transmission media.
The propagation delay depends on the propagation speed of the media, which is 3 × 108 meters/second in a vacuum and normally much less in a wired medium; it also depends on the distance of the link.
In other words, propagation delay is

## Slide 9
Processing Delay
The processing delay is the time required for a router or a destination host to receive a packet from its input port, remove the header, perform an error detection procedure, and deliver the packet to the output port
Delaypr = Time required to process a packet in a router or a destination host
Queuing Delay
Queuing delay can normally happen in a router.
A router has an input queue connected to each of its input ports to store packets waiting to be processed; the router also has an output queue connected to each of its output ports to store packets waiting to be transmitted.
The queuing delay for a packet in a router is measured as the time a packet waits in the input queue and output queue of a router.

## Slide 10
end